## Slide 1: WORKSHOP ON PCB DESIGNING
WITH ALTIUM

## Slide 2: What is PCB
Printed Circuit Board
Electronic Board that connects circuit components
PCB populated with electronic components is a printed circuit assembly (PCA)
PCBs are rugged, inexpensive, and can be highly reliable
Mass manufacturing
Professional

## Slide 3: Materials of PCB
Conducting layers are typically made of thin copper foil.
The board is typically coated with a solder mask that is green in color. Other colors that are normally available are blue and red.
Unwanted copper is removed from the substrate after etching leaving only the desired copper traces or pathways

## Slide 4: Parts of a PCB
Components
Pads
Traces
Vias
Top Metal Layer
Bottom Metal Layer

## Slide 5: Steps in PCB design
Film Generation
2. Shear Raw Material
3. Drill Holes
Industry standard 0.059" thick, copper clad, two sides

## Slide 6: Steps in PCB design
4. Electrolus copper
Apply copper in hole barrels
5. Apply Image
Apply Photosensitive Material to develop selected areas from panel

## Slide 7: Steps in PCB Design
6. Strip and Etch
Remove dryfilm, then etch exposed copper
Tin protects the copper circuitry from being etched
7. Solder Mask
Apply solder mask area to entire board with the exception of solder pads

## Slide 8: Steps in PCB Design
8. Solder Coat
9. Silkscreen
Apply white letter marking using screen printing process
Apply solder to pads

## Slide 9: INTRODUCTION TO ALTIUM DESIGNER

## Slide 10: Creating a New PCB Project
START THE ALTIUM DESIGNER BY DOUBLE CLIKING ON ICON.

## Slide 11
Select File»New»Project»PCB Project from the menus
Creating a New PCB Project

## Slide 12
The Projects panel will open, displaying the new project file, PCB_Project1.PrjPCB (with no documents added).
Creating a New PCB Project

## Slide 13
THERE IS NO FILES IN THE PROJECT.
SO WE HAVE TO ADD FIRST THE SCHEMETIC FILE TO DRAW CIRCIUIT.
Creating a New Schematic Sheet

## Slide 14
THEN YOU CAN SEE THE PAGE LIKE GINVEN BELOW.
Creating a New Schematic Sheet

## Slide 15
NOW MAKE ONE NEW FOLDER AS PER UR REQUIRED NAME IN D OR E DRIVE TO SAVE THE PROJECT.
NOW SAVE THE PROJECT AS GIVEN BELOW.
Creating a New Schematic Sheet

## Slide 16
WE CAN GET ALL THE REQUIRED COMPONENT AND CONNECTORS FROM THE LIBRERIES GIVEN IN THE
RIGHT SIDE OF UR SCHEMETIC DIAGRAM.
NOW OPEN THE LIBRARAY TO ADD DIFF COMPONENTS AND CONNECTORS AS REQUIRED.
Creating a New Schematic Sheet

## Slide 17
TO ADD COMPONENT FROM THE LIST JUST DRAG IT FROM LIST AND DROP IT TO SCHEMETIC DIAGRAM.
ADD REQUIRED CONNECTORS LIKE IC OR MALE FEMALE CONNECTORS FROM THE LIST.
Creating a New Schematic Sheet

## Slide 18
NOW FIRST GIVE THE NAMES TO THE ALL THE COMPONENT AND CONNECTORS AT THE PLACE P? D? R?.
YOU CAN GIVE NAME AS R1 R2 R3… D1 D2 D3… IC1 IC2 IC3…
NOW TO CONNECT THE COMPONENT AND CONNECTOR TAKE PLACE WIRE AND CONNECT AS PER REQUIRMENT.
ALSO SAVE THE PROJECT FILE.
Creating a New Schematic Sheet

## Slide 19: Make a Schematic for given circuit